## Slide 1: Build Your Own Router
Computer Networks
Project 2

## Slide 2: Project Overview
Implement a simple router in a single router topology with static routing table (forwarding table).
Your router will receive raw Ethernet frames, and handle/forward packets in correct logic.

## Slide 3: Lessons to learn

## Slide 4: What is a Router?
Forwarding: move packets from router’s input to appropriate router output
Routing: determine route taken by packets from source to dest.

## Slide 5: What about Our Router?
Forwarding: move packets from router’s input to appropriate router output
  Load predefined routing table
  Look up matching entry in routing table
Handle ICMP
Handle ARP request / reply
Routing: determine route taken by packets from source to dest.

## Slide 6: Link Layer
Transfer internet layer datagram from node to adjacent node over a link
Encapsulate internet layer datagram into frame, add header & trailer
Use “MAC” address in frame headers for source, dest

## Slide 7: MAC address v.s. IP address
32-bit IP address:
  network-layer address
  used to get datagram from src to dest IP subnet
48-bit MAC (Ethernet) address:
  link-layer address for network interfaces
  get frame from one interface to another physically-connected interface (same subnet)
  Broadcast address: “FF:FF:FF:FF:FF:FF”

## Slide 8: Ethernet Frame
56 bit
48 bit
48 bit
16 bit
32 bit
Need in this project
Encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
  preamble and crc are handled transparently in this project

## Slide 9: ARP: Address Resolution Protocol
ARP request: request IP-MAC mapping of next hop interface (send to broadcast address)
ARP reply: send IP-MAC of current interface
ARP cache: IP – MAC mapping for nodes (timeout after a 30s)
Question: How to get MAC address of B from B’s IP address

## Slide 10: ARP: Address Resolution Protocol
Walkthrough: send datagram from A to B through R.
Volunteer?

## Slide 11: Internet Protocol (IPv4)
Delivering packets from src to dest based on IP address
Header checksum
Decrement TTL

## Slide 12: Routing Table
Destination & Netmask: subnet network ID
Gateway: next hop IP address to destination
Interface: name of network interface card connected to gateway
Metric: routing metric of path to destination (omitted in this project)

## Slide 13: Longest Prefix Match
Destination | Netmask | Gateway | Interface
0.0.0.0 | 0.0.0.0 | 10.0.1.100 | eth3
192.168.2.2 | 255.255.255.0 | * | eth1
172.64.3.10 | 255.255.0.0 | * | eth2
Where should packet dest at “192.168.1.1” go?

## Slide 14: Longest Prefix Match
Destination | Netmask | Gateway | Interface
0.0.0.0 | 0.0.0.0 | 10.0.1.100 | eth3
192.168.2.2 | 255.255.255.0 | * | eth1
172.64.3.10 | 255.255.0.0 | * | eth2
Where should packet dest at “192.168.2.1” go?

## Slide 15: ICMP: Internet Control Message Protocol
Used by hosts & routers to communicate network-level information
  error reporting (unreachable host, network, port, protocol)
  echo request/reply
Sent as IPv4 payload
Content: Internet header + 8 bytes of original datagram

## Slide 16: Ping & Traceroute
Ping: ICMP echo request/reply
  reply with TTL = 64

## Slide 17: Ping & Traceroute
Ping: ICMP echo request/reply
  reply with TTL = 64
Traceroute: displaying possible routes and RTT in IP network.
  sends UDP segments with TTL = 1,2,3, … with unlikely port number
  when nodes receive datagram with TTL=0, return ICMP “Time Exceeded”
  destination returns ICMP “Port Unreachable”

## Slide 18: Useful Materials
IPv4:
  RFC 791: https://tools.ietf.org/html/rfc791
  Text Book: section 4.4.1, 4.4.2
ICMP:
  RFC 792: https://tools.ietf.org/html/rfc792
  Text Book: section 4.4.3
ARP:
  RFC 826: https://tools.ietf.org/html/rfc826
  Text Book: section 5.4.1

## Slide 19: results to show

## Slide 20: Expected Behaviors
ping from client to any server & router interfaces
traceroute from client to any server & router interfaces
wget files from server
Update ARP cache table

## Slide 21: Ping
ping from client to any http servers

## Slide 22: Ping
ping wrong IP address

## Slide 23: Traceroute
traceroute to any http server
traceroute to router interfaces

## Slide 24: File Downloading
wget from any of servers

## Slide 25: ARP Cache table
“pingall”
30 seconds later

## Slide 26: code to implement

## Slide 27: Code Structure

## Slide 28: Key Methods
NEED TO IMPLEMENT
Method that receives a raw Ethernet frame (simple-router.hpp|cpp):

## Slide 29: Key Methods
IMPLEMENTED
Method to send raw Ethernet frames (simple-router.hpp|cpp):

## Slide 30: Key Methods
NEED TO IMPLEMENT
Method to handle ARP cache events (arp-cache.hpp|cpp):

## Slide 31: Key Methods
NEED TO IMPLEMENT
Method to lookup entry in the routing table (routing-table.hpp|cpp):

## Slide 32: issues to notice

## Slide 33: Some Important Issues
Grading (up to 105%)
  Router Implementation (85%=45%public + 40%private)
    Ping tests (50%)
    Traceroute tests (20%)
    File Downloading tests (15%)
  Project Report + Code Quality (20%)
Individual work

## Slide 34: Some Important Issues
Submission
  Source code (“make tarball”)
  Do not modify existing data structures
  Report: no longer than THREE pages
Evaluation
  ping, traceroute, file downloading, details in project spec
  Code quality
  Project report

## Slide 35: Some Important Issues
Start up: today, after class
Deadline: 12.5, 23:59 (3 weeks and a half)
Late Submission: 12.6 ~ 12.12, 23:59
  -20pts punishment
  No more submissions after 12.12

## Slide 36: Problems Emerged
Improper TTL handling in traceroute / ping
  when to do TTL--?
  when to send ICMP time exceeded?
Fail to maintain ARP cache entries / send ARP requests
Imperfect longest prefix match
Compilation & project structure problem
  check before submission

## Slide 37
Get to work as soon as possible, not like FTP!

## Slide 38: Q&A
Good luck

## Slide 39: Acknowledgement
This project is based on the CS118 class project by Alexander Afanasyev, UCLA.